## Slide 1: TCP Session Hijacking
An attacker takes over a TCP session between two machines.
Server
trust message from C
Based on C’s IP address
Client (C)
Attacker
Impersonate C

## Slide 2: TCP Session Hijacking
Server
trust message from C
Based on C’s IP
Client (C)
SYN (seq=x)
SYN ACK (ack=x+1 seq=y)
ACK (ack=y+1,seq=x+1)
“echo + + > ~/.rhosts” (ack=y+1,seq=x+1)

## Slide 3: TCP Session Hijacking
Server
trust message from C
Based on C’s IP
SYN (seq=x)
SYN ACK (ack=x+1 seq=y)
ACK (ack=y+1,seq=x+1)
“echo + + > ~/.rhosts” (ack=y+1,seq=x+1)
Attacker
RST
Ignore the command as this session is not established from C

## Slide 4: TCP Session Hijacking
IP Spoofing
Server
trust message from C
Based on C’s IP
Client (C)
Attacker
SrcIP | DstIP | IP Payload
C’s IP | Server IP | ……..
Notes: Will this packet be sent to the server?

## Slide 5: TCP Session Hijacking
Client (C)
Server
trust message from C
Based on C’s IP
SrcIP: C, DstIP: Server
SYN (seq=x)
SrcIP: C, DstIP: Server
ACK (ack=?,seq=x+1)
Attacker
SrcIP: Server, DstIP: C
SYN ACK (ack=x+1 seq=y)
Notes: Will this packet be sent to the server?

## Slide 6: TCP Session Hijacking
Client (C)
Server
trust message from C
Based on C’s IP
SrcIP: C, DstIP: Server
SYN (seq=x)
SrcIP: C, DstIP: Server
ACK (ack=?,seq=x+1)
Attacker
SrcIP: Server, DstIP: C
SYN ACK (ack=x+1 seq=y)
If the attacker can predict “y”, it can complete the establishment of the session
Notes: Will this packet be sent to the server?

## Slide 7: Predict the Initial Sequence Number in Berkeley-Derived Systems
The Berkeley-derived kernels
  Increment the initial sequence number variable by a constant once per second(e.g., 128,000)
  Increment the initial sequence number variable by another constant for each new connection (e.g., 64,000)
Attacker can
  initiate a legitimate connection and observe the initial sequence number used
  then calculate the initial sequence number used for the next connection attempt

## Slide 8: TCP Session Hijacking
Client (C)
Server
trust message from C
Based on C’s IP
SrcIP: C, DstIP: Server
SYN (seq=x)
SrcIP: C, DstIP: Server
ACK (ack=y,seq=x+1)
Attacker
SrcIP: Server, DstIP: C
SYN ACK (ack=x+1 seq=y)
The attacker predicts “y”
Notes: Will this packet be sent to the server?

## Slide 9: TCP Session Hijacking
Client (C)
Server
trust message from C
Based on C’s IP
SrcIP: C, DstIP: Server
SYN (seq=x)
SrcIP: C, DstIP: Server
ACK (ack=y,seq=x+1)
Attacker
SrcIP: Server, DstIP: C
SYN ACK (ack=x+1 seq=y)
The attacker predicts “y”
“echo + + > ~/.rhosts”
(ack=y+1,seq=x+1)
Notes: Will this packet be sent to the server?

## Slide 10: TCP Session Hijacking
Client (C)
Server
trust message from C
Based on C’s IP
SrcIP: C, DstIP: Server
SYN (seq=x)
SrcIP: C, DstIP: Server
ACK (ack=y,seq=x+1)
Attacker
SrcIP: Server, DstIP: C
SYN ACK (ack=x+1 seq=y)
The attacker predicts “y”
“echo + + > ~/.rhosts”
(ack=y+1,seq=x+1)
RST
Notes: Will this packet be sent to the server?

## Slide 11: TCP Session Hijacking
Client (C)
Server
trust message from C
Based on C’s IP
SrcIP: C, DstIP: Server
SYN (seq=x)
SrcIP: C, DstIP: Server
ACK (ack=y,seq=x+1)
Attacker
SrcIP: Server, DstIP: C
SYN ACK (ack=x+1 seq=y)
The attacker predicts “y”
“echo + + > ~/.rhosts”
(ack=y+1,seq=x+1)
RST
Flooding
Notes: Will this packet be sent to the server?

## Slide 12: TCP RST
A TCP reset basically kills a TCP connection instantly.
  If the RST bit is set to 1, it indicates to the receiving computer that the computer should immediately stop using the TCP connection; it should not send any more packets using the connection's identifying numbers, called ports, and discard any further packets it receives with headers indicating they belong to that connection.

## Slide 13: Malicious Usage: RST Reset
Client (C)
Attacker (inline)
SYN ACK (ack=x+1 seq=y)
Server
SYN (seq=x)
SYN ACK (ack=x+1 seq=y)
ACK (ack=y+1,seq=x+1)
Sniff
Inject
RST (Src Server)
RST (Src Client)

## Slide 14: Who is “Malicious”/Malicious?
Computer 1
Address: IP1
Computer 2
Address: IP2

## Slide 15: Who is “Malicious”/Malicious?
The “Great Fire Wall” (active now).
Comcast’s actions to disrupt P2P connections (around 2007).

## Slide 16: RST Reset
Great Firewall (from wiki)

## Slide 17: The Paper
“Detecting Forged TCP Reset Packets”, N. Weaver, Robin Sommer, and Vern Paxson.
Computer 1
Address: IP1
Computer 2
Address: IP2
Forged TCP RST

## Slide 18: Discussion
Why don’t they design GFW like this (inline interruption) rather than RST-based method (out-of-band interruption)?
If(c exchanges sensitive content with S)
{discard all traffic in this session}
Client (C)
Server
Notes: Performance
Failure

## Slide 19: Discussion
Why does GFW send RST packets to both client and server?
  GFW can send RST to only client. It should be enough to terminate the connection.

## Slide 20: The Normal Case of RST
Server
Seq: X, Ack: Y
(pkt with len1)
Seq: (X+ Len1), Ack: (Y + Len2) or 0
RST
Client (C)
Seq: Y, Ack: (X + Len1)
(pkt with len2)

## Slide 21: The Injection of RST
Server
Seq: X, Ack: Y
Seq: (X+ Len1), Ack: 0
RST
Client (C)
Seq: Y, Ack: (X + Len1)
Attacker: Observe
Attacker: sending
What is the problem?

## Slide 22: Race Condition
The sender can send a few (decided by both congestion control and flow control algorithms) packets with out receiving acknowledgments.
  Seq number < Min(window-size, rwnd)
    Window-size for congestion control, decided by the sender of the packet
    rwnd for flow control, decider by the receiver of the packet.

## Slide 23: The Challenge
Server
Seq: X, Ack: Y
(pkt with len1)
Seq: (X+ Len1), Ack: Y+len2
RST
Client (C)
Seq: Y, Ack: (X + Len1); pkt len2
Attacker: Observe
Attacker: sending
What is the problem?
Seq: (X+len1), Ack: (Y+len2)
Pkt with len3
Objective: X+len1+len3 <= seq <= X+len1+len3+rwnd

## Slide 24: The Solution
Server
Seq: X, Ack: Y
(pkt with len1)
Seq: (X+ Len1), RST
Client (C)
Seq: Y, Ack: (X + Len1); pkt len2
Attacker: Observe
Attacker: sending
Seq: (X+len1), Ack: (Y+len2)
Pkt with len3
Objective: X+len1+len3 <= seq <= X+len1+len3+rwnd
Seq: (X+ Len1 + W), RST
Seq: (X+ Len1 + 2W), RST

## Slide 25: Detection Rules
RST_SEQ_DATA:
  The RST packet is “out of sequence”, with the receiver observing a sequence number less than the preceding data packet would suggest.
  What doesn’t it happen for normal cases?
DATA_SEQ_RST:
  The receiver will see further data packets from the sender after it has already received the RST.
  What doesn’t it happen for normal cases?

## Slide 26: Detection Rules
RST_SEQ_CHANGE:
  Back-to-pack pairs of RSTs in which the second RST has a sequence number higher than the first, and that exceeds the current maximum sequence number.
  What doesn’t it happen for normal cases?

## Slide 27: Detection Rules
RST_ACK_CHANGE:
  Nonsensical ACK numbers
SYN_RST
  SYNs immediately followed by RST
SYN_ACK_RST
  SYN/ACKs immediately followed by RST

## Slide 28: Application Layer Attacks
The Application Layer
  A variety of protocols
  DNS

## Slide 29: Domain Name System (DNS)
Indispensable component for the Internet
  www.google.com -> 173.194.75.106
Used by a huge percentage of Internet applications
  Browsers
  FTP
  Instant Messengers

## Slide 30: How DNS Works
cash.foo.com
Recursive
DNS server
Root server
com server
(IP: Y.Y.Y.Y)
foo server
(IP: Z.Z.Z.Z)
“.com” server IP?
“foo.com” server IP?
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
Y.Y.Y.Y
Z.Z.Z.Z
Domain | IP
cash.foo.com | X.X.X.X

## Slide 31: How DNS Works
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
A UDP Packet
A UDP Packet

## Slide 32: DNS Poisoning Attack
How a recursive server accepts a response from the authoritative server
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 

## Slide 33: DNS Poisoning Attack
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: m.m.m.m foo.com: z.z.z.z |  | 
Control

## Slide 34: The Challenges for Attackers
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: m.m.m.m foo.com: z.z.z.z |  | 
Guess Source Port: 1024 - 65535
Guess ID: 0 - 65535

## Slide 35: The Challenges for Attackers
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
Guess Source Port: 1024 - 65535
Guess ID: 0 – 65535
…
Before the authentic response arrives
Notes: Before

## Slide 36: How to Address Challenges?
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
Guess Source Port: 1024 - 65535
Guess ID: 0 – 65535
…
Before the authentic response arrives
cash.foo.com
cash.foo.com
……
Notes: Before

## Slide 37: Inline DNS Injection
“The Collateral Damage of Internet Censorship by DNS Injection”
  Sparks, Neo, Tank, Smith, and Dozer, Sigcomm 2012

## Slide 38: How DNS Works
cash.foo.com
Recursive
DNS server
Root server
com server
(IP: Y.Y.Y.Y)
foo server
(IP: Z.Z.Z.Z)
“.com” server IP?
“foo.com” server IP?
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
Y.Y.Y.Y
Z.Z.Z.Z
Domain | IP
cash.foo.com | X.X.X.X

## Slide 39: How DNS Injection Works
cash.foo.com
Recursive
DNS server
Root server
com server
(IP: Y.Y.Y.Y)
foo server
(IP: Z.Z.Z.Z)
“.com” server IP?
“foo.com” server IP?
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
Y.Y.Y.Y
Z.Z.Z.Z
Domain | IP
cash.foo.com | X.X.X.X
cash.foo.com
Recursive
DNS server
Root server
com server
(IP: Y.Y.Y.Y)
“.com” server IP?
“foo.com” server IP?
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
Y.Y.Y.Y
T.T.T.T
Attacker (inline)

## Slide 40: Where does it start
https://lists.dns-oarc.net/pipermail/dns-operations/2010-March/005260.html

## Slide 42: Collateral Damage
Collateral damage occurs when a DNS query from a recursive resolver enters a censored network, causing the censorship mechanism to react.

## Slide 43: Collateral Damage
US
All networks along the path of the query are suspicious
Recursive
DNS server
Root/TLD/Authoritative Server
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
CN
JP

## Slide 44: A Network?
An organization can have a collection of IP addresses
  E.g., corresponding to a subnet
An IP address can be attributed to an organization
  130.108.224.196
  whois 130.108.224.196
  whois -h whois.cymru.com " -v 130.108.224.196"

## Slide 45: Example
Traceroute
Mapping the IP of an router into its ASN/organization

## Slide 46: Search for Injected Paths: Honey-Query
US
Recursive
DNS server
Root/TLD/Authoritative Server
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
CN
JP
Fields | Values
Destination IP | ?
Domain name | ?

## Slide 47: Search for Injected Paths: Honey-Query
US
Recursive
DNS server
Root/TLD/Authoritative Server
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
CN
JP
Fields | Values
Destination IP | Pick up an address from /24 network. (how many /24 different networks?) This address does not run DNS service. (WHY?)
Domain name | Domains that are commonly considered as “sensitive”

## Slide 48: Honey-Query
What do you expect after you send out the honey-query?
  Not censored?
  Censored?

## Slide 49: Honey-Query
What do you expect after you send out the honey-query?
  Not censored?
    No DNS response at all.
  Censored?
    A DNS response
    Is the IP address in the response trustable?

## Slide 50: Identify the Injector
Client
pkt
ICMP response
R1
R2
R3
R4
TTL Value | Source IP address of the ICMP packet
1 | R1
2 | R2
3 | R3
4 | R4
Server

## Slide 51: Identify the Injector
Recursive
DNS server
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
R1
R2
R3
R4
TTL Value | Source IP address of the ICMP packet
1 | R1
2 | R2
3 | R3
4 | R4 + (A DNS response)

## Slide 52: Some Statistics

## Slide 53: Do not forget
All honey queries are sent from real IP addresses controlled by authors
These IP addresses are unlikely to reside in the censored networks
Censors should actually not censor these IP addresses
But they inject fake DNS responses anyway
  “the DNS injector does not consider packet origin when injecting packets”.
  Why?