## Slide 1: Networking Vulnerabilities
This lecture is mainly based on the powerpoint slides by Prof. Mark Stamp, Prof. Lawrie Brown, Dr. Junjie Zhang
Notes: In this lecture, we will discuss a number of protocol vulnerabilities. These vulnerabilities are majorly intrinsic to the design of the protocol and independent of the implementation of these protocols.

## Slide 2: IP Spoofing
The Network (IP) Layer
  Above the Ethernet-layer
application
transport
network
Data link
physical

## Slide 3: IP Spoofing
Sending an IP packet with forged source IP address
To impersonate another host with respect its IP address
Applications
  Denial of Service Attacks
  Access the IP-based authentication services such as the R services suite (rlogin, rsh, etc.)

## Slide 4: IP Spoofing
Send a packet to a networked computer
Computer 1
Address: IP1
Computer 2
Address: IP2
The Internet
IP2
payload
IP1

## Slide 5: IP Spoofing
Send a packet to a networked computer with a forged source IP address
Computer 1
Address: IP1
Computer 2
Address: IP2
The Internet
IP2
payload
IP3

## Slide 6: Transport Layer Attacks
The Transport Layer
  TCP & UDP Protocols

## Slide 7: SYN Flood Attack
Denial-of-Service (DoS) Attack
  An attack used to cause a machine/service unable to perform its essential functionality
SYN flood
  A specific type of denial-of-service attack
  Targeting at the implementation of the TCP protocol

## Slide 8: The TCP 3-Way Handshake
Client (IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN ACK (ack=x+1 seq=y)
ACK (ack=y+1,seq=x+1)
Listening
Initialize a data structure in the memory
Wait
Connected
(IP1, Port1, TCP, Seq, AcK, …)
Update the data structure
Notes: Allocate memory for the data structure used to maintain the state of the connection

## Slide 9: An Incomplete TCP 3-Way Handshake
Client (IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN ACK (ack=x+1 seq=y)
Listening
Initialize a data structure in the memory
(IP1, Port1, TCP, Seq, AcK, …)
Release the memory for this data structure
A timeout period
Notes: Timeout period: configurable, like one minute
Attacker sends many connection requests
  Spoofed source addresses
Victim allocates resources for each request
  Connection requests exist until timeout
  Old implementations have a small and fixed bound on half-open connections
Resources exhausted  requests rejected
No more effective than other channel capacity-based attack today

## Slide 10: SYN Flood Attack
IP1
IP, Port
Server
Memory
IP1, port1, IP, Port, SYN
IP1, port3, IP, Port, SYN
IP1, port4, IP, Port, SYN
IP1, ………., IP, Port, SYN
……
Notes: Two disadvantages:
IP1 is bad (fixed)
Only 2^16 connections

## Slide 11: SYN Flood Attack
IP1
IP, Port
Server
Memory Filled Up!
IP2, port1, IP, Port, SYN
IP3, port3, IP, Port, SYN
IP4, port4, IP, Port, SYN
IPN, …….., IP, Port, SYN
……
Spoofed Source IP addresses
Notes: Two disadvantages:
IP address is spoofed, then you the attacker can send 2^48 SYN packets to the server (theoretically, bounded by the attacker’s network bandwidth), to exhaust the memory space of the server.

## Slide 12: Distributed SYN Flood Attack
IP, Port
Rnd_IP, Rnd_Port, IP, Port, SYN
Memory Filled Up!
……
Notes: Early detection of Denial of service attack is important.
When a server detects Denial of service attack, the server should scale up the service (Maybe by using the cloud service)
Once a server receives a lot of SYN packets, it should realize that it is under attack..
Using UDP. UDP does not maintain the state. The application maintains the state.
TCP/IP is usually implemented by the Operating System.

## Slide 13: SYN Cookies
General idea
  Delay the initialization of the data structure to the third packet in the 3-way handshake
Client (IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN-ACK
(ack=x+1 seq=y)
ACK
(ack=y+1,seq=x+1)
(IP1, Port1, TCP, Seq, Ack, …)
Client (IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN-ACK
(ack=x+1 seq=y)
ACK
(ack=y+1,seq=x+1)
(IP1, Port1, TCP, Seq, Ack, …)
Notes: For the second picture, an attacker can send send a fake ACK message to the server.
How does the server know:
The client has sent the SYN packet in the first place.
The client has successfully received the SYN-ACK packet?

## Slide 14: SYN Cookies
Client (IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN-ACK
(ack=x+1 seq=y)
t mod 32
5 bits
MSS
3 bits
Cookie=HMAC(t, Ns, SIP, SPort, DIP, DPort)
t mod 32: t is a slowly increasing timestamp maintained by the server, ensuring sequence numbers increase every 64 seconds
MSS: encoding of server MSS (maximum segment size)
Cookie: easy to create and validate, hard to forge
Ns: the secret shared by all the connections
No resource is invested in the server side to maintain the state of this connection!!
Notes: For the second picture, an attacker can send send a fake ACK message to the server.
Server sequence number: t mod 32, MSS, Syn cookie.
Cookie=HMAC(t, Ns, SIP, SPort, DIP, DPort)
Ns: the secret shared by all the connections
How does the server know:
The client has sent the SYN packet in the first place.
The client has successfully received the SYN-ACK packet?

## Slide 15: SYN Cookies
Client (IP1, Port1)
Server (IP2, Port2)
ACK
(ack=K, seq=D)
(IP1, Port1, TCP, Seq, Ack, …)
K – 1
5 bits
3 bits
24 bits
Equal to “t mod 5”?
Equal to HMAC(t,Ns,SIP,Sport,DIP,Dport)?
Resource is invested in the server side to maintain the state of this connection if “YES” for both questions.
Notes: For the second picture, an attacker can send send a fake ACK message to the server.
How does the server know:
The client has sent the SYN packet in the first place.
The client has successfully received the SYN-ACK packet?

## Slide 16: SYN Cookies: Legitimate User
Client (IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN-ACK
(ack=x+1 seq=y)
ACK
(ack=y+1,seq=x+1)
t mod 32
5 bits
MSS
3 bits
Cookie=HMAC(t, Ns, IP1, Port1, IP2, Port2)
Ack – 1  (y+1) – 1  y;
Notes: For the second picture, an attacker can send send a fake ACK message to the server.
How does the server know:
The client has sent the SYN packet in the first place.
The client has successfully received the SYN-ACK packet?

## Slide 17: SYN Cookies: SYN Flood and ACK Flood
Client (Fake-IP1, Port1)
Server (IP2, Port2)
SYN (seq=x)
SYN-ACK
(ack=x+1 seq=y)
No resource is invested in the server side to maintain the state of this connection!!
Client (Fake-IP1, Port1)
Server (IP2, Port2)
ACK
(ack=K, seq=D)
t mod 32
MSS
Cookie=HMAC(t, Ns, SIP, SPort, DIP, DPort)
Attacker need to correctly forge the HMAC to enable the initialization of the data structure in the server side.
Notes: For the second picture, an attacker can send send a fake ACK message to the server.
How does the server know:
The client has sent the SYN packet in the first place.
The client has successfully received the SYN-ACK packet?

## Slide 18: TCP RST
A TCP reset basically kills a TCP connection instantly.
  If the RST bit is set to 1, it indicates to the receiving computer that the computer should immediately stop using the TCP connection; it should not send any more packets using the connection's identifying numbers, called ports, and discard any further packets it receives with headers indicating they belong to that connection.

## Slide 19: Malicious Usage: RST Reset
Client (C)
Attacker (inline)
SYN ACK (ack=x+1 seq=y)
Server
SYN (seq=x)
SYN ACK (ack=x+1 seq=y)
ACK (ack=y+1,seq=x+1)
Sniff
Inject
RST (Src Server)
RST (Src Client)

## Slide 20: Who is “Malicious”/Malicious?
Computer 1
Address: IP1
Computer 2
Address: IP2

## Slide 21: Who is “Malicious”/Malicious?
The “Great Fire Wall” (active now).
Comcast’s actions to disrupt P2P connections (around 2007).
Notes: Single egress point

## Slide 22: RST Reset
Great Firewall (from wiki)
Notes: Drop packets (a middle packets maintaining states of the packets), that is too expensive.

## Slide 23: The Paper
“Detecting Forged TCP Reset Packets”, N. Weaver, Robin Sommer, and Vern Paxson.
Computer 1
Address: IP1
Computer 2
Address: IP2
Forged TCP RST

## Slide 24: Application Layer Attacks
The Application Layer
  A variety of protocols
  DNS

## Slide 25: DNS
If you want to…
  Call someone, you need to ask for their phone number
    You can’t just dial “P R O F G I L L ”
  Mail someone, you need to get their address first
What about the Internet?
  If you need to reach Google, you need their IP
  Does anyone know Google’s IP?
Problem:
  People can’t remember IP addresses
  Need human readable names that map to IPs

## Slide 26: Domain Name System (DNS)
Indispensable component for the Internet
  www.google.com -> 173.194.75.106
Used by a huge percentage of Internet applications
  Browsers
  FTP
  Instant Messengers
Destination | IP
www.google.com | 173.194.75.106
…….. | …….
Notes: Solution: A Centralized Database: DNS system (IP address is public, known to everybody.) What is the problem? How many computers connected to the internet that need to use the DNS service? A huge number of DNS requests. Incoming traffic, outgoing traffic, and DNS queries to the DNS database. Insert of new domain name: time consuming.
Centralized DNS system database: registration, query.
Hierarchy DNS service: tree structure.

## Slide 27: DNS at a High-Level
Domain Name System
Distributed database
  No centralization
Simple client/server architecture
  UDP port 53, some implementations also use TCP
  Why?
Hierarchical namespace
  As opposed to original, flat namespace
  e.g. .com  google.com  mail.google.com
  Top level domain (.com), second level domain (.google), third level domain (.mail)
Notes: Top level domain (.com), second level domain (.google), third level domain (.mail)

## Slide 28: Naming Hierarchy
Top Level Domains (TLDs) are at the top
Maximum tree depth: 128
Each Domain Name is a subtree
  .edu  neu.edu  ccs.neu.edu  www.ccs.neu.edu
Name collisions are avoided
  neu.com vs. neu.edu
Root
edu
com
gov
mil
org
net
uk
fr
etc.
neu
mit
ccs
ece
husky
www
login
mail

## Slide 29: Hierarchical Administration
Tree is divided into zones
  Each zone has an administrator
  Responsible for the part of the hierarchy
Example:
  CCIS controls *.ccs.neu.edu
  NEU controls *.neu.edu
Root
edu
com
gov
mil
org
net
uk
fr
etc.
neu
mit
ccs
www
login
mail
ICANN
Verisign
Notes: ICANN's mission is to help ensure a stable, secure, and unified global Internet.
The Internet Corporation for Assigned Names and Numbers (ICANN /ˈaɪkæn/ EYE-kan) is an American multistakeholder group and nonprofit organization responsible for coordinating the maintenance and procedures of several databases related to the namespaces and numerical spaces of the Internet, ensuring the network's stable and secure operation.

## Slide 30: How DNS Works
cash.foo.com
Recursive
DNS server
Root server
com server
(IP: Y.Y.Y.Y)
foo server
(IP: Z.Z.Z.Z)
“.com” server IP?
“foo.com” server IP?
“cash.foo.com” IP?
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
cash.foo.com: X.X.X.X
foo.com: Z.Z.Z.Z
Y.Y.Y.Y
Z.Z.Z.Z
Domain | IP
cash.foo.com | X.X.X.X
Notes: DNS service uses UDP service.
recursive DNS server
root server
top level domain server
second level domain server (authoritative server, belonging to the owner)
third level domain server

## Slide 31: How DNS Works
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
A UDP Packet
A UDP Packet

## Slide 32: DNS Poisoning Attack
How a recursive server accepts a response from the authoritative server
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
Notes: Recursive DNS server: local network (maintain a cache), a proxy.
The other computers in the enterprise network can use the cached IP address for the domain names

## Slide 33: DNS Poisoning Attack
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: m.m.m.m foo.com: z.z.z.z |  | 
Control
Notes: The attacker does not know the port number of the recursive server, and the query ID.
The attacker can send back many fabricated DNS responses.
The recursive DNS server's source port number is incremental.

## Slide 34: The Challenges for Attackers
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x foo.com: z.z.z.z |  | 
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: m.m.m.m foo.com: z.z.z.z |  | 
Guess Source Port: 1024 - 65535
Guess ID: 0 - 65535

## Slide 35: The Challenges for Attackers
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
Guess Source Port: 1024 - 65535
Guess ID: 0 – 65535
…
Before the authentic response arrives
Notes: one fabricated DNS response: 1/ (2^16 -1024)*2^16 (16 bits of port number – 1024 ports, 16 bits of ID)
N fabricated DNS response: N / (2^16-1024) *2^16
N fabricated DNS response, for M DNS queries for the same domain name: N*M / (2^16-1024) *2^16

## Slide 36: How to Address Challenges?
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
Guess Source Port: 1024 - 65535
Guess ID: 0 – 65535
…
Before the authentic response arrives
cash.foo.com
cash.foo.com
……
Notes: Fabricated DNS responses match any of the three DNS requests.
If the client sends out 3 DNS queries, then the recursive DNS server will generate and send out
three DNS queries to the DNS server, then the attacker's DNS response has a higher probability to be accepted.
one fabricated DNS response: 1/ (2^16 -1024)*2^16 (16 bits of port number – 1024 ports, 16 bits of ID)
N fabricated DNS response: N / (2^16-1024) *2^16
N fabricated DNS response, for M DNS queries for the same domain name: N*M / (2^16-1024) *2^16

## Slide 37: Counteracting DNS Posioning
0x20
https://astrolavos.gatech.edu/articles/increased_dns_resistance.pdf

## Slide 38: General Objective of 0x20
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x |  | 
Can we find more bits to increase the randomness of the DNS responses from the authority server without changing the protocol?
Guess Source Port: 1024 - 65535
Guess ID: 0 - 65535

## Slide 39: General Idea of 0x20
How does a authoritative DNS server usually create the response?
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cash.foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cash.foo.com: x.x.x.x |  | 
copy

## Slide 40: General Idea of 0x20
How does a authoritative DNS server usually create the response?
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cAsh.Foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | ?: x.x.x.x |  | 
copy

## Slide 41: General Idea of 0x20
SrcIP | SrcPort (16 bits) | DstIP | DstPort (53)
ID (16 bits) | Query: cAsh.Foo.com |  | 
cash.foo.com
Recursive
DNS server
foo server
(IP: Z.Z.Z.Z)
cash.foo.com: X.X.X.X
SrcIP | SrcPort (53) | DstIP | DstPort (16 bits)
ID (16bits) | cAsh.Foo.com: x.x.x.x |  | 
copy
If the recursive DNS server randomly pick the upper case or lower case for each letter in “cash.foo.com”, and it verifies the letter case in the response, how many DNS responses that an attacker needs to generate for poisoning attacks?
Guess Source Port: 1024 - 65535
Guess ID: 0 – 65535
Guess the upper and lower case for each letter: 2^10
Notes: www.Microsoft.com vs. www.ibm.com
www.163.com

## Slide 42: 0x20 in a Nutshell
The DNS recursive server randomly decides the upper and lower case of a letter in a DNS query with respect to the domain name
Issue the query to the authority server and get response whose ID/Port number is consistent with the request/query
Check whether the letter case is consistent with that in the query for each letter in the domain name

## Slide 43: The Applicability of 0x20
The implementation of DNS authority server
  Does it faithfully copy the domain name from a query to a response?
The nature of the domain
  Length
    0x20 is more powerful for www.microsoft.com than www.ibm.com
  The number of numeric characters
    0x20 is more powerful for www.ibm.com than www.123.com